Technical requirements for water butterfly check valves and butterfly valve

Water butterfly check valves

Water butterfly check valves (wafer type) are meant for complete shutoff and regulation of the volume of potable water SanPiN 2.1.4.1074, of heating-system water SanPiN 2.04.07 and for other non-aggressive liquids at temperatures from 5 to 90 °С and at pressures of up to1.6 MPa (10 kilogram-force/cm2). Leak tightness class according to GOST 9544 (100% Leak-Tight closure: leaks are not allowed).

Materials:

- Body – cast iron GG-25

- Disc – noncorrosive steel 12X18H10T

- Shaft – noncorrosive steel 40X13

- Seat – EPDM

Butterfly valves

Butterfly valves (wafer type) are used to prevent backflow in systems designed for unidirectional flow according to SanPiN 2.1.4.1074, SanPiN 2.04.07 and for other non-aggressive liquids at temperatures from 5 to 90 °С and at pressures of up to1.6 MPa (10 kilogram-force/cm2). Leak tightness class according to GOST 9544 (100% Leak-Tight closure: leaks are not allowed).

Materials:

- Body – cast iron GG-25

- Disc - noncorrosive steel 12X18H10T

- Shaft – noncorrosive steel 40X13

- Spring – noncorrosive steel 40X13

- Seat – EPDM