1. Assembling the SHARK cabin

Assemble the SHARK service lift close to its final place of installation. Assemble both versions, sliding doors and double doors, as follows:

Installation holes have been pre-drilled. Bolts, nuts etc can be found in the plastic bags supplied.

- Assemble the right, left and bottoms sections with the cabin resting on its back.

- Mount the roof spine and then slide the roof into position and fit to the cabin.

- Fit the wire guides.

- Mount the traction hoist and safety brake to the spine.

- Attach the cabin front.

- Mount the 4 bottom rubber feet to the bottom of the cabin.

- Mount the operation limit stop switch and emergency limit stop switch on the roof using the contact bracket.

- Attach the bottom safety stop beam including the wires that hold the bottom safety stop

beam.

- Bring the cabin to its upright position.

- Mount the doors on the cabin. On the Double door version - remember to install the ground wire at the top hinge.

- Mount the steps and handle inside the cabin.

- Feed the power cable through the rear hole and fit the socket to the back using the strips.

- Mount the bottom safety stop switch and adjust. Connect the switch cables to the power cabinet according to the colour code. All wires are secured using strips (max 200mm between strips).

All bolts and nuts are stainless steel.

DANGER!

If it is possible to enter underneath the service lift a double button safety stop

must be fitted. (See Installation Manual pages 34-36).