Системы поения и системы подогрева воды

При любой температуре корова нуждается в большом количестве воды. Поилки из стали предназначены для поения 40-50 коров. Сильный проток воды 120 л/мин позволяет ей быть чистой. Поилки размещаются в коровнике в зависимости от количества коров в группе и размещения самих групп.

Длина поилки – от 1,00 м до 3,00 м

Высота поилки – 80 – 100 см

Снабжение поилок теплой водой происходит посредством специальной системы подогрева воды. Установка оборудована регулятором температуры и автоматическим ограничителем температуры. Длина водопровода – до 250 м. Установку можно эксплуатировать при температуре до -40º. Корпус циркуляционного насоса и платформы выполнен из нержавеющей стали. Тэн 3 кВт.

Световые коньки.

Световые коньки – это надежный и эффективный способ улучшить систему вентилирования в существующем коровнике. Для хорошо функционирующей естественной вентиляции коровник ставят поперек главного направления ветра. Таким образом, давление ветра способствует лучшему оттоку воздуха из коровника. За счет высоких отражателей ветра  сохраняется свободный отток воздуха из коровника.

- Лучший отток воздуха благодаря идеальной форме конька

- Приспособляемость к величине и типу постройки

- Интенсивное попадание дневного света

- Экономия энергии за счёт отсутствия электрических вентиляторов

- Здоровый, сухой воздух, необходимый как для персонала, так и для скота

- Пол, стены и крыша остаются сухими

- Сотовый поликарбонат прочнее стекла в 200 раз, что значительно увеличивает срок его эксплуатации

- Высокая пропускная способность света и устойчивость при сильных перепадах температур

- Превосходные изолирующие свойства

- Противовоспламеняющиеся свойства

- Устойчивость поликарбоната к царапинам и трению

Поликарбонат выдержал испытания снежной нагрузкой до 350 кг/м² и давлением ветра до 250 кг/м².

Проем для конька: 80-250 см

Выход воздуха: 24, 36, 54 см

Уклон конька: 22,5º

Вентиляционные шторы.

Вентиляционные шторы могут быть различных вариантов исполнения: однослойные или двойные, открывающиеся, складываясь сверху вниз, скручиваясь снизу вверх или открывающиеся сверху, скручиваясь к низу одним приводом, также комбинированные. Изготавливаются, как правило, из полиэтиленового прозрачного тента белого цвета, материал различается по степени рассеивания ветра (при изменении размера ячеек) и количеству пропускаемого ультрафиолета.

- Управление электрическим или ручным приводом

- Регулятор штор

- Реверсивное переключение для электродвигателей переменного  трехфазного тока

Возможность определения внутренней и наружной температуры воздуха, скорости и направления ветра, дождя и снегопада

Автоматические станции выпойки телят.

Благодаря автоматической станции выпойки телят становится возможным рациональное кормление телят либо на основе молочного порошка, либо цельного молока. Станция может быть установлена в любом месте телятника и запрограммирована как на групповое, так и на одиночное кормление.

- Автоматы рассчитаны на группы по 20, 40 и 100 телят.

- Встроенная идентификация теленка по нашейному респондеру.

- Автоматическая промывка поилки щелочным или кислотным раствором.

- Дезинфекция соски после каждого теленка.

- Подогрев и перемешивание смеси для выпойки.

- Дозирование жидких и порошковых медикаментов и подкормок.

- Удобное меню управления автоматом на русском языке.

Встроенное считывающее устройство автомата по респондеру на шее теленка и в соответствии с запрограммированным рационом допускает теленка к питью.

В автомате ведется учет всех данных, когда-либо полученных им, он предоставляет информацию, когда провести обезроживание теленка и выполнить плановую вакцинацию, определяет активность теленка по числу подходов к станции, замеряет, с какой скоростью теленок выпивает свою порцию, и, соответственно, выявляет возможное заболевание. Также возможно составление разных рационов для телочек и бычков и определение стоимости теленка при том или ином графике выпойки.

Удобна функция самообслуживания, когда автомат для облегчения диагностики составляет отчеты о собственном состоянии и возникших неполадках.

Автомат исключает возможные негативные последствия человеческого фактора: не допоили теленка, плохо промыли ведро, температура молока не соответствует температуре выпойки, не выдержаны пропорции вода/ЗЦМ, не позаботились о гигиене рук и пр.

Длина х Ширина х Высота: 50 см х 50 см х 95 см

Необходимое давление воды: от 2 до 4 бар

Напряжение / сила тока: 230 В/16 А

Оптимальный размер загона для группы в 30 телят: 110-120 м²

Индивидуальные домики для телят.

Преимущества использования индивидуальных домиков для телят очевидны: постоянный свежий воздух, изоляция от источников инфекции, индивидуальное наблюдение и уход, соблюдение необходимой технологии кормления телят с разным развитием, свобода движения и т.д. В тыловой части домика за счет значительной длины (2,2 м) создается воздушный тамбур и теленком поддерживается необходимый микроклимат. У домика нет дна, поэтому для лучшей теплоизоляции на площадку, где устанавливается домик, насыпают подушку из крупных опилок 5-7 см, а сверху делают глубокую подстилку из соломы. Солома периодически подсыпается, обновляя верхний слой подстилки, емкости для корма крепятся к вольеру, поэтому на уход не требуется много времени.

Электронные весы для коров.

Марка ВТЭ 8904-1000СХ

Цена поверочного отделения и дискретность отсчета – 1 кг

Предел взвешивания: от 10 до 1000 кг

Предел допускаемой погрешности в интервале от 10 до 250 кг: +/- 0,5 г

Предел допускаемой погрешности в интервале от 250 кг до 1000 кг: +/- 1 кг

Габаритные размеры: 1000 х 2200 х 2000 мм

Масса: 250 кг

Щетки для чистки коров.

Щетка осуществляет не только чистку коров и удаление паразитов, но и выполняет массажные функции.

- Включается посредством поднимания

- Изменяет направление вращения при перегрузе

- Водо- и пыленепроницаемый двигатель

- Легкость в монтаже на стену или на стойку и простота в обслуживании

- Напряжение: 230В/50Гц

- Потребляемая мощность: 0,37 кВт

- Число оборотов: 60 об/мин

Ворота для животноводческих помещений

Секционные ворота

Полотно ворот, состоящее из секций, расположенных друг над другом, в открытом положении не занимает ценного пространства. Экономя место, полотно перемещается под потолок помещения и освобождает проезд полностью.

Техника для сельского хозяйства.

Особая форма кормораздатчика позволяет совместить кормосмеситель малых габаритов с вертикальным типом микса, что обеспечивает однородность и мягкость при измельчении и перемешивании продукта. Буксируемые кормосмесители серии TRIPLEX снабжены 3 вертикальными спиралевидными шнеками дифференциального диаметра с ножами (5 ножей на шнеке). Возможность измельчения рулонов без предварительной резки.

Резчики-погрузчики силоса

Резчики силоса предназначены для резки всех видов силоса (из сенажа и т.п.) в виде блоков из наземных силосов максимальной высотой 1,4 м и их транспортировки в хлев.

Машина подвешивается непосредственно на трёхточечной системе подвеса тягача или на переднем погрузчике, а внешняя гидравлическая система должна быть оборудована двумя соединительными гнёздами. Работа резчиком заключается во вбивании вил в призму силоса, вырезке трёх сторон блока, поднятии его вверх и транспортировке в хлев.

Режущий комплект резчика в животноводстве даёт значительные преимущества, а именно:

- возможность хранения вырезанных блоков силоса в кормовом коридоре в течение нескольких дней, без ухудшения качества корма благодаря ненарушенной структуре.

- гладкая поверхность среза препятствует проникновению воздуха внутрь блока, а тем самым защищает силос от гниения;

- ограничение нарушения покоя животных и ограничение доступа холодного воздуха в помещение;

- возможность одновременного кормления несколькими видами силоса, например, кукурузы, травы (блоки силоса при установке чередуются);

- возможность индивидуальной дозировки, как количества, так и вида кормов, в зависимости от необходимости.

Максимальная высота призмы: 140 см

Объём вырезаемого блока: 0,6 м³

Максимальная масса вырезаемого блока: 800 кг

Собственная масса: 350 кг

Длина / ширина / высота: 1,22/ 1,12/ 0,90 м

Оборудование для приготовления комбикормов.

Дробилка.

Тип дробилки - молотковый

Диаметр сита: 4, 5, 6мм (круглые)

Мощность электродвигателя: 15 кВт, 18,5кВт, 22кВт

Производительность: до 2000 кг/час

Габариты дробилки: 800х800х900мм

Материал, предназначенный для дробления, направляется гибкой всасывающей трубой на молотковую голову. Измельченный материал после перехода через сито выбрасывается действием ротора в выпускной патрубок и дальше гибким напорным трубопроводом транспортируется в кормосмеситель.

Смеситель.

Тип смесителя: шнековый

Объем: 4,4 куб.м.

Два смотровых люка с задвижками

Контрольные окошки состояния заправки емкости

Приемник для загрузки добавок и разгрузочный канал

Габаритные размеры смесителя: 2900 х 1700 мм

Смеситель состоит из следующих узлов: емкости с основанием, мешалки кормов, привода. Емкость с основанием составляет конструкцию, сваренную из стали и профилей. Мешалка кормов состоит из вертикального шнекового транспортера. Смеситель снабжен насыпом (для ручной погрузки), патрубком для пневматической погрузки, разгрузочным каналом, двумя смотровыми люками с задвижками, контрольными окошками состояния заправки емкости. За 20 минут процент смешивания достигает 96-98%.

Весы

Электронные (предел взвешивания 2500 кг.)

Механические (предел взвешивания 2500 кг.)

Погрузчик зерна пневматический

Технические характеристики:

Тип вентиляционной установки центробежный, двухступенчатый.

- Производительность до 15 т/ч

- Напряжение питания, 380 В

- Установленная мощность электропривода, 22 кВт

- Диаметр приемного и выдающего трубопроводов, 160 мм

- Максимальная длина приемного трубопровода, 40 м

- Максимальная длина выдающего трубопровода, 100 м

- Максимальная высота установки циклона выгрузки, 10 м

- Габариты2100х1250х1900

- Масса350кг

Установка предназначена для транспортировки зерновых: погрузка, выгрузка, в том числе ж/д вагонов, переброска. Подача в бункеры, накопители, в машины. Установка маневренная, легко передвигается вручную. Транспортная магистраль сборно-разборная, быстро монтируемая. Отсутствует соприкосновение продукта с лопастями вентилятора, следовательно, не происходит повреждение семенного материала.

Культиватор

Культиваторы типа Smaragd выполняют весь комплекс сезонных полевых работ за один обрабатывающий проход. Работа происходит без забивания рабочих органов (даже при значительном количестве органической массы). Точное заглубление культиватора и регулировка рабочей глубины. Значительное снижение веса за счет применения высоколегированных сталей.

Тип: Smaragd 4000

Мощность: 150 л.с.

Число лемехов: 9/4

Ширина захвата: 4000 мм

Высота рамы (междурядье): 800/800 мм

Производительность (при 10 км/час): 4 га/час

Максимальная скорость: 16 км/час

Вес: 1785 кг

Тип: Smaragd 6000

Мощность: до 191 кВт, 260 л.с.

Число лемехов: 13/6

Ширина захвата: 6000 мм

Высота рамы (междурядье): 800/800 мм

Производительность (при 10 км/час): 6 га/час

Максимальная скорость: 12 км/час

Вес: 3083 кг

Косилки.

Прицепные дисковые косилки с эффективной поворотной системой.

Модели GMS/GCS представляют серию прицепных дисковых косилок. Эти машины созданы в кооперации с фермерами по всему миру, благодаря чему дисковые косилки GMS/GCS представляют собой надежные и проверенные машины, сильными сторонами которых являются:

Повышение рабочей скорости за счет уникальной системы безопасности

Одной из особенностей машин, делающей их особенно эффективными, является система Top Safe. Она позволяет работать на более высокой скорости и таким образом повышает производительность. Система Top Safe защищает машину от вибрации и неровностей поля, что позволяет работать на более высокой скорости без потери качества и риска повредить машину.

Простое управление. Косилки GMS/GCS очень удобны в эксплуатации. Управление функциями осуществляется быстро и эффективно, кроме того, у оператора постоянно хороший обзор всей машины со своего рабочего места.

Косилка фронтальная Z-015.

- Очень экономичный вариант для крупных хозяйств

- Подгребатели формируют ровный покос шириной до 2 м

- Компактней усиленный косилочный брус

- Скользящие полозья из износоустойчивой стали

- Плавная регулировка высоты среза

- Ножи увеличенной длины до 115 мм

- Возможность формирования двух покосов

- Ширина захвата: 3,70 м

- Ширина прокоса: до2м

- Количество ножей: 18 (9x2)

- Обороты ВОМ: 1000 об/мин

- Мощность трактора: 70 л.с.

- Производительность: 4,0 га/час

- Количество дисков: 9

Пресс-подборщики.

Пресс-подборщики серии CORSA— это традиционное конструктивное качество Маскар отвечающее требованиям надёжности, высокой производительности, простоты и экономии пользователя.

Стандартный захват 1,70м или широкий (2м), снаряжённый двумя транспортёр-устройствами.

Частые стержни: стандартные для сильного и более постоянного давления по всей поверхности рулона.

Ротор: облегчает вход продукта в предкамеру, избегая переполнения или замедления.

Переменная колея: позволяет работу на холмах и на сложных почвах.

Высокая плотность благодаря механическим крюкам, которые налаживают закрытие заднего люка и позволяют создание более тяжёлых рулонов.

Стержень для давления: позволяет производить наладку плотности рулона согласно продукту, который нужно прессовать.

Электрическое сигнальное устройство предупреждает прямо с кабины тягача, что камера полна.

Налаживаемый тяговый руль с возможностью наладить высоту от земли до рамы машины, чтобы приспособить машину к разным моделям тягачей.

- Гидравлический подъем/опускание подборщика

- Обвязка шпагатом в одну нить

- Механический запуск обвязывания

- Механическая регулировка степени плотности прессования

- Электрическое оборудование

- Механический счетчик тюков

- Устанавливаемое на 2 точки дышло

- Карданный вал с режущим болтом

- Акустический и оптический сигнал заполнения камеры

- Обмотчики рулонов

Самозагружающаяся машина для обмотки рулонов предназначена для загрузки на стол машины и обматывания рулонов из сена трав и других растений с влажностью около 60%, свернутых в рулоны при помощи сматывающих прессов. После обмотки рулоны предназначены для силосования (заготовок) на силосованный корм.

Травы и другие мотыльковые растения, предназначенные для силосования и обмотки, необходимо косить в первой фазе покоса (желательно после полудня). По истечении 10-15-ти часов просушивания (на следующий день после покоса в благоприятных погодных условиях) должен быть проведен сбор скошенного материала при помощи сматывающих прессов. Степень прессования рулонов должна быть максимальной

Практически сразу после замотки прессом (максимально в течение 2 часов) следует обмотать рулоны на обматывающей машине. В рулонах, оставленных на длительное время, наступит нежелательный процесс гниения. Рулоны после обмотки нужно уложить (соблюдая особенную осторожность, чтобы не испортить плёнку) минимум на 6-8 недель на гладкой и сухой поверхности. Процесс ферментации в обмотанных рулонах должен проходить при положительных температурах. Обмотанные рулоны можно хранить в два слоя. По истечении двух месяцев сено-силос пригоден для скармливания в качестве полноценного корма.

Грабли-ворошилки.

Грабли-ворошилки колесно-пальцевые сконструированы на базе трубы повышенной толщины для обеспечения максимальной прочности. Независимые и взаимозаменяемые сгребающие колеса монтированы на конических роликоподшипниках. Несущая структура с гидравлическим подъемом в 3 точках. Система амортизации позволяет сгребающим колесам адаптироваться к любому типу поверхности для сгребания, ворошения или оборачивания.

- Пальцы сгребающих колес изготавливаются из особой стали.

- Диаметр сгребающих колес – 140 см.

- Шарнирная ходовая часть и независимые сгребающие колеса позволяют адаптироваться к любым условиям работы.

- Гидравлическая регулировка открытия/закрытия и позиционирования сгребающих колес.

- Мануальная регулировка ширины рабочего поля

- Центральное сгребающее колесо с гидравлической регулировкой подъема.

- Количество пальцев в одном сгребающем колесе – 40 шт.

Преимущества:

- Валок травы не скручивается, а остается мягким даже при высокой влажности массы.

- Благодаря оригинальной форме пальцев в сочетании с амортизационными пружинами на колесах происходит полное копирование микрорельефа почвы, что позволяет без потерь убирать всю кормовую массу и одновременно минимально травмировать почву.

- Валок не загрязняется землей и камнями

- Грабли легко переводятся в рабочее положение и складываются в транспортное с помощью гидросистемы трактора.

- Грабли без потерь убирают высоко- и низкоурожайные травостои.

- Невысокая стоимость технического обслуживания.

- Высокая рабочая скорость (до 30 км/час).

- Полная автоматизация рабочего процесса.

Валкообразователи.

Валкообразователь с укладкой валка сбоку R 1405 S

Преимущества:

- Съемные граблины и складываемые защитные дуги

- Большая производительность

- Возможность получить один валок за три прохода

- Регулируемая ширина захвата

- Сдвоенный валок 13,0/13,40 – 2 одинарных валка 5,80/6,05 м

- Съемные граблины MIN-trans – миним. транспортная ширина 1,60/2,20 м

- Стальные шестерни, гипоидная передача

- Однотяговое прицепное устройство

- 12 граблин на 1 рабочий корпус, тангенциальное ведение

- Гидравлическая регулировка рабочей ширины и подъема корпусов

- Высокое поднятие пальцев при повороте и транспортировке

- Колеса расположены близко к пальцам граблин

- Регулировка наклона секций

- Валкообразователь с укладкой валка сбоку S 1810 Pro

Преимущества:

- Оптимальная ширина захвата для трактора от 40 кВт/55 л.с.

- Шасси с поворотными колесами, максимальная стабильность работы, минимальная транспортная ширина

- Закрытый редуктор капсульного типа с жидкой смазкой

- Съемные граблины

- Управление Vario – минимальный радиус поворота

- Необслуживаемые граблины, стальные подшипники

- Ролики направляющей 47 мм

- Карданный вал с увеличенным углом поворота

- Регулировка высоты работы каждой секции

- Бесступенчатая корректировка работы граблин

- Подъем рабочих корпусов при разворотх до 50 см

- Кормоуборочные комбайны JF-STOLL

Дойной корове при продуктивности 30 л/день требуется в 4 раза больше энергии, чем сухостойной корове. Поэтому требуется высокое качество кормов. Ежедневный период пережевывания дойной коровы с высоким удоем составляет примерно 10 часов. Хорошо измельченные грубые корма снижают время пережевывания на 20 %. Поэтому потребность в питательных веществах полностью обеспечивается, что снижает потребность в концентрированных кормах

Все машины оснащаются ножами с вольфрамовым покрытием, заточным камнем с быстрой установкой, возможностью реверса, противорежущей пластиной с вольфрамовым покрытием с возможностью оборота на 180º. Ножи ротора расположены по секциям для быстрой замены. Высокую производительность также обеспечивает широкий ротор. Возможно оснащение травяной и кукурузной жаткой. На всех машинах установлен гидравлический подъем подборщика. Комбайн заготавливает корма как прямым комбайнированием, так и подбирая с валка с последующим измельчением. Высокая производительность измельчающего барабана за счет раздвижения питающих валов. Резка в направлении выброса снижает потребляемую мощность на 25 - 50 %.

Кормоуборочные комбайны KRONE.

Самоходный полевой измельчитель BiG X.

BiG X - самоходный кормоуборочный комбайн с точной длиной резки. Скорость движения по дороге 40 км/час в серийном исполнении. Благодаря новаторской концепции гидростатического привода и характеристикам движения, как у легкого автомобиля, комбайн движется на более низких оборотах двигателя быстрее, что позволяет экономить до 25 процентов топлива. Гидравлический привод подпрессовывающих вальцов и возможность настраивать длину резки из кабины, не прерывая движения. Новейшие технологии, высокий рабочий комфорт, качество измельчения высочайшего уровня.

Подборщик EasyFlow.

Две модели подборщиков фирмы KRONE с шириной захвата 3 м или 3,8 м. С шестью граблинами и расстоянием между зубьями 55 мм, при любых условиях, подборщик работает без потерь и не пропускает ни одного стебля. Крепкая и прочная конструкция делает серийный подборщик EasyFlow сверхпрочным агрегатом.

Копирование рельефа почвы: все кормоуборочные приставки всегда безупречно копируют рельеф почвы при помощи маятниковой рамы. Для переезда на другое поле, боковые копирующие колеса убираются при помощи гидравлической системы.

Подборщик EasyFlow работает без сложного механизма управления граблинами, т.е. в конструкции отсутствует множество деталей, подверженных интенсивному износу - беговая дорожка и ролики граблины. Особенностью конструкции, позволившей отказаться от механизма управления граблинами, является волнообразный сегмент в зоне погружения граблин и увеличенная рабочая скорость вращения граблин. Больше нет проблем с наматыванием кормовой массы. Для этого агрегата характерен надежный и производительный подбор. Оснастка подборщика также впечатляет: он оборудован шестью граблинами, причем их консоли имеют дополнительную опору. Другие технические детали: гидравлический привод подборщика с бесступенчатым изменением частоты вращения, гидравлическое управление копирующими колесами для движения по дорогам, гидравлически поднимаемый прижимной валец, а также раздельные защитные устройства для подборщика и подающего шнека.

Гидравлический привод с большим диапазоном частоты вращения. Частота вращения от 300 и до 700 об/мин регулируется бесступенчато из кабины. Или можно активировать режим автоматической настройки частоты вращения к скорости движения машины, и использовать большие возможности BiG X в полном объеме.

Жатка прямого среза XDisc

Жатка прямого среза XDisc оснащена дисковым косилочным механизмом EasyCut. Кормовая масса скашивается с высочайшим качеством среза и направляется на подающий шнек диаметром 0,90 м. Большой шнек надежно транспортирует также и тяжелую длинностебельную массу к питающим вальцам кормоуборочного комбайна. Частота вращения режущего аппарата может настраиваться бесступенчато посредством гидравлического привода прямо из кабины.

Ширина захвата 6,20 м. Прямая уборка силосной массы или биомассы. Закрытый и тысячи раз проверенный косилочный брус.

Swilling and water heating systems

A cow requires a plenty of water at any temperature. Drinking bowls from steel are intended for swilling of 40-50 cows. The strong water channel of 120 l/mines allows it to be pure. Drinking bowls are placed in a cowshed depending on quantity of cows in a group and accommodations of these groups.

Length of a drinking bowl - from 1.00 m up to 3.00 m

Height of a drinking bowl - 80 - 100 sm

Supply of drinking bowls by warm water occurs by means of special water heating system. Installation is equipped by a temperature regulator and the temperature automatic terminator. Length of a waterpipe - up to 250 m. Installation can be maintained at the temperature up to -40º. The case of the circulating pump and the platform is executed from stainless steel. Tan of 3 kw.

Light skates.

Light skates are a reliable and an effective way to improve an aeration system in the existing cowshed. Cowshed is put across a mainstream of the wind for well functioning natural ventilation. Thus, the wind pressure promotes the best air outflow from cowshed. Due to high wind reflectors free air outflow from the cowshed is kept.

· 	 The best air outflow owing to the ideal form the skate

· 	 Adaptability to size and type of construction

· 	 Intensive hit of a daylight

· 	 Economy of energy due to absence of electric fans

· 	 The healthy, dry air are necessary both for the personnel, and for the cattle

· 	 The floor, walls and a roof stay dry

· 	Honeycomb polycarbonate is stronger than glass in 200 times, that considerably increases the term of its exploitation

· 	 High throughput of light and stability at strong differences of temperatures

· 	 Excellent isolating properties

· 	 Properties against combustible

· 	 Stability of polycarbonate to scratchs and friction

Polycarbonate has stood tests by snow loading up to 350 kg/m2 and wind pressure up to 250 kg/m2.

Aperture for skate: 80-250 sm

Air output: 24, 36, 54 sm

Bias of skate: 22.5º

Ventilating curtain

Ventilating curtains can be various variants of execution: single-layered or double, opening, developing from top to bottom, rolling from bottom to top or opening from a top, rolling to a bottom one drive, also combined. Ventilating curtains are made, as a rule, from a white polyethylene transparent awning, the material differs on a degree of the wind dispersion (at change of the size of cells) and to quantity of a passed ultraviolet.

· 	Control of an electric or manual drive

· 	 The curtains regulator

· 	 Reversive switching for electric motors of a variable three-phase current

Definition opportunity of internal and external air temperature, speed and direction of the wind, rain and snowfall.

Calves swilling automatic stations

There is possible a rational calves feeding either on the basis of a dairy powder, or whole milk owing to calves swilling automatic stations. The station can be established in any place of the calfshed and it is programmed both on group, and on single feeding.

· 	 Automatic devices are calculated on groups of 20, 40 and 100 calves.

· 	 The built in identification of a calf on the neck-responder.

· 	 Automatic washing a drinking bowl by an alkaline or acid solution.

· 	 Dummy disinfection after every calf.

· 	 Heating and mixing of a mixture for swilling.

· 	 Batching liquid and powder medicines and additional feeding

· 	 The convenient menu of automatic device control in Russian.

The built in automatic reading out device on the responder on a calf’s neck and according to the programmed diet supposes the calf to drink.

There is conducted the account of all data ever received in the automatic device, it gives the information when to make calf disinfection and to execute scheduled vaccination, defines calf activity on the number of approaches to the station, measures, with what speed a calf drinks his portion, and, accordingly, reveals possible disease. Also drawing up of different diets for the heifers and the bulls and a calf cost definition is possible at this or that swilling schedule.

Function of self-service is convenient when the automatic device for diagnostics simplification makes reports on own condition and the arisen malfunctions.

The automatic device excludes possible negative consequences of the human factor: have swilled a calve not enough, have badly washed out a bucket, the temperature of milk mismatches swilling temperature, proportions are not sustained, have not taken care of hands hygiene and so on.

Length х Width х Height: 50 sm х 50 sm х 95 sm

Necessary water pressure: from 2 up to 4 bar

Pressure / current force: 230 В/16 A

The optimum size of a shelter for group in 30 calves: 110-120 m

Individual small houses for calves

Advantages of using of individual small houses for calves are obvious: constant fresh air, isolation from infection sources, individual supervision and leaving, observance of necessary calves feeding technology with different development, freedom of movement, etc. Due to significant length (2,2) in a rear part of a small house is created air tambour, the necessary microclimate is supported by a calf. The small house does not have bottom, therefore for the best heat isolation on a platform a pillow from large sawdust of 5-7 sm are filled where the small house is established, and from above a deep laying of straw are done. Straw is periodically poured, updating the top of a laying, capacities for a fodder fasten to an open-air cage, therefore leaving is not required a lot of time.

Electronic balances for cows.

Mark VTE 8904-1000СХ

The branch testing price and readout step-type behaviour - 1 kg

Weighing limit: from 10 up to 1000 kg

Supposed error limit in an interval from 10 up to 250 kg: +/-0.5 g

Supposed error limit in an interval from 250 kg up to 1000 kg: +/-1 kg

Overall dimensions: 1000 х 2200 х 2000 mm

Weight: 250 kg

Brushes for cows cleaning

The brush carries out not only cows cleaning and parasites removal, but also carries out massage functions.

· 	 Joins by means of raising

· 	 Changes a direction of rotation at overload

· 	 Water and the dustproof engine

· 	 Ease in installation on a wall or on a rack and simplicity in service

· 	 The Pressure: 230V/50 Hertz

· 	 Power consumption: 0.37 kw

· 	 Number of turns: 60 rev/min

Gate for cattle-breeding premises

Section gate

The gate cloth consisting from sections, located on each other, in the open position does not borrow valuable space. The cloth moves under a ceiling of a premise and releases travel completel saving a place.

Technics for an agriculture

The special form of food-feeder allows to combine small dimensions fodder-mixer with vertical mix type that provides uniformity and softness at crushing and hashing of a product. Towed fodder-mixer series TRIPLEX are supplied 3 vertical helicoid screws differential diameter with knifes (5 knifes on a screw). An opportunity of crushing of rolls without preliminary cutting.

Silo carvers-loaders

Silo carvers are intended for sharping all kinds of a silo (from hay, etc.) in the form of blocks from ground silos in the maximal height of 1.4 m and their transportations in a shed.

The machine is suspended directly on three-dot tractor suspending system or on a forward loader, and the external hydraulic system should be equipped by two connecting jacks. Work with the carver consists in driving in a silo prism, a cutting of three parties of the block, its raising upwards and transportation in a shed.

The carver cutting complete set gives significant advantages in animal industries, namely:

·          An storage opportunity of the cut out silo blocks in a fodder corridor during several days, without fodder deterioration owing to not broken structure.

· 	 The smooth cut surface interferes air penetration inside the block that protects a silo from rotting;

· 	 Infringement restriction of animals rest and cold air access restriction in a premise;

· 	 An simultaneous feeding opportunity by the several kinds of a silo, for example, corn, a grass (blocks of a silo at installation alternate);

· 	 An individual dosage opportunity, both quantity, and a kind of fodders, depending on necessity.

The maximal height of a prism: 140 sm

Cut volume of the out block: 0.6 m3

The maximal weight of the cut out block: 800 kg

Own weight: 350 kg

Length / width / height: 1.22/1.12/0.90 m

The equipment for mixed fodders preparation

Crusher

Type of a crusher – hammering

Diameter of a sieve: 4, 5, 6 mm (round)

Capacity of the electric motor: 15 kw, 18,5 kw, 22 kw

Productivity: up to 2000 kg/hours

Dimensions of a crusher: 800х800х900mm

The material for crushing is gone on a hammering head by a flexible soaking up pipe. After transition through a sieve the crushed material is thrown out in a final branch pipe by action of a rotor and further is transported in fodder-mixer by the flexible pressure head pipeline.

The fodder-mixer

Type of the fodder-mixer: screwing

Volume: 4.4 m3

Two viewing hatches with latches

Condition control windows of capacity refuelling

The receiver for loading additives and the unloading channel

Overall dimensions of the fodder-mixer: 2900 х 1700 mm

The fodder-mixer consists of following units: capacities with the basis, fodder-mixers, drive. The capacity with the basis makes a design welded from steel and structures. The fodder-mixers consist from vertical screwing conveyor. The fodder-mixer is supplied terrace (for manual loading), a branch pipe for pneumatic loading, the unloading channel, two viewing hatches with latches, condition control windows of capacity refuelling. For 20 minutes the percent of mixing reaches 96-98 %.

Balances

Electronic (weighing limit 2500 kg.)

Mechanical (weighing limit 2500 kg.)

Grain pneumatic loader

Characteristics:

Type of ventilating installation is centrifugal it has two-level.

· 	 Productivity up to 15 tone/hour

· 	 The feed pressure: 380V

· 	 The established capacity of the electric drive, 22 kw

· 	 Diameter of reception and giving out pipelines, 160 mm

· 	 The maximal length of the reception pipeline, 40 m

· 	 The maximal length of the giving out pipeline, 100 m

· 	 The maximal height of an unloading cyclone installation, 10 m

· 	Overall dimensions: 2100х1250х1900

· 	Weight: 350 kg

Installation is intended for transportation grain: loading, unloading, including iron-road cars, transference. Submission in bunkers, stores, in machines. Installation is maneuverable and easily moves manually. A transport highway is collapsible and quickly mounted. There is no contact of a product with blades of the fan, hence, there is no damage of a seed material.

Cultivator

Cultivators of Smaragd type carry out all complex of seasonal field works for one processing pass. Work occurs without hammering of working bodies (even at a significant amount of organic weight). Exact a depthing cultivator and working depth adjustment. Significant weight reduction due to application high-alloy steels.

Type: Smaragd 4000

Capacity: 150 h.p.

Number of ploughshare: 9/4

Width of capture: 4000 mm

Height of a frame (between rows): 800/800 mm

Productivity (at 10 km/hours): 4 hectares/hours

The maximal speed: 16 km/hours

Weight: 1785 kg

Type: Smaragd 6000

Capacity: up to 191 kw, 260 h.p.

Number of ploughshare: 13/6

Width of capture: 6000 mm

Height of a frame (between rows): 800/800 mm

Productivity (at 10 km/hours): 6 hectares/hours

The maximal speed: 12 km/hours

Weight: 3083 kg

Mowers

Hook-on disk mowers with effective rotary system.

Models GMS/GCS represent a series of hook-on disk mowers. These machines are created in cooperation with farmers worldwide owing to what disk mowers GMS/GCS represent the reliable and checked up machines which strengths are:

Increasing working speed due to safety unique system.

The Top Safe system is one of features of the machines doing them especially effective. It allows to work on higher speed and thus it raises productivity. System Top Safe protects the machine from vibration and field roughnesses that allows to work on higher speed without loss of quality and risk to damage the machine

Simple management. Mowers GMS/GCS are very convenient in operation. Control of functions is carried out quickly and effectively, besides at the operator constantly good review of all machine from the workplace.

Face-to-face mower Z-015

· 	 Very economic variant for large-scale enterprises

· 	 Rowing up machine form an equal mowing in width up to 2 m

· 	 More compactly a strengthened scything bar

· 	 Sliding runners from deterioration-steady steel

· 	 Smooth adjustment of cut height

· 	 Knifes of the increased length up to 115 mm

· 	 The opportunity of two mowing formations

· 	 Width of capture: 3.70 m

· 	 Width of mowing: up to 2 m

· 	 Quantity of knifes: 18 (9x2)

· 	 Turns ВОМ: 1000 rev/min

· 	 Capacity of a tractor: 70 h.p.

· 	 Productivity: 4.0 hectares/hours

· 	 Quantity of disks: 9

Press-sorters

Press-sorters of CORSA series are traditional constructive quality Maskar meeting the requirements of reliability, high efficiency, simplicity and economy of the user.

Standard capture: 1.70 m or wide (2m), equipped two conveyor-devices.

Frequent cores: standard for strong and more constant pressure on all surface of a roll.

Rotor: facilitates an input of a product in the prechamber, avoiding overflow or delay.

Variable track: allows to work on hills and on complex soils.

High density owing to mechanical hooks which adjust closing the back hatch and allow creation of heavier rolls.

Core for pressure: allows to adjust roll density according to a product which needs to be pressed.

The electric alarm device warns directly from the tractor’s cabin that the chamber is full.

Adjusted traction rudder has an opportunity to adjust height from the ground up to the machine’s frame of the to adapt the machine for different models of tractors.

· 	Sorter hydraulic rise/lowering

· 	A lace by a twine in one string

· 	 Mechanical start of lacing

· 	 Mechanical adjustment of a pressing density degree

· 	 The electric equipment

· 	 The bales mechanical counter

· 	 A lace beam established on 2 points

· 	 A cardan shaft with a cutting bolt

· 	 The acoustic and optical signal of chamber filling

· 	 Rolls winding

The self-loaded machine for the rolls winding is intended for loading on the machine’s table and winding of rolls from hay of grasses and other plants with humidity about 60 % curtailed into rolls by means of taking up presses. After a winding rolls are intended for siloing (preparations) on a silo fodder.

Grasses and others papilionaceous plants intended for siloing and a winding, it is necessary to mow grasses in the first mowing phase (it is desirable after midday). After 10-15 hours of drying (next day after a mowing in favorable weather conditions) gathering of the mowing material by means of winding presses should be lead. The degree of rolls pressing should be maximal.

Practically right after winding by press (it is maximal within 2 hours) it is necessary to wind rolls by the winding machine. There will come rotting undesirable process in the rolls left for long time. After a winding rolls need to be laid (observing especial care not to spoil a film) a minimum for 6-8 weeks on a smooth and dry surface. Fermentation process in the wound rolls should pass at positive temperatures. The wound rolls can be stored in two layers. After two months hay-silo is suitable for feeding as a high-grade fodder.

Raker-agitator

Wheel-manual raker-agitators are designed on the raised thickness pipe basis for maintenance of the maximal durability. Independent and interchangeable raking up wheels assemble on conic roller bearings. Bearing structure has hydraulic rise in 3 points. An amortization system allows to adapt raking up wheels for any type of a surface for raking up, tedding or turning over.

· 	 Raking up wheels ringers are made of special steel.

· 	 Diameter of raking up wheels - 140 sm

· 	The articulate running part and independent raking up wheels allow to adapt for any operating conditions.

· 	 Hydraulic adjustment of opening/closing and positioning of raking up wheels.

· 	 Manual adjustment of width of a working field

· 	 The central raking up wheel with hydraulic adjustment of rise.

· 	 Quantity of fingers in one raking up wheel - 40 pieces

Advantages:

· 	 Grass roll does not braided, it remains soft even at high humidity of weight.

· 	 There is a full copying of a ground microrelief in a combination to amortisation springs on wheels owing to the original form of fingers that allows to clean all fodder weight loss-free and simultaneously minimally to injure ground.

· 	 Roll does not become soiled the ground and stones

· 	 The rakers are easily translated into position and develop in transport by means of a tractor hydrosystem.

· 	 The rakers clean high- and lowyielding herbages loss-free.

· 	 Low cost of maintenance service.

· 	 High working speed (up to 30 km/hours).

· 	 Full automation of working process.

Roll-generators

Roll-generator with roll stacking sideways R 1405 S

Advantages:

· 	 Demountable rakers and put protective arches

· 	 Greater productivity

· 	 The opportunity to receive one roll for three passes

· 	 Adjustable width of capture

· 	 Dual roll 13.0/13.40 - 2 unary rolls 5.80/6.05 m

· 	 Demountable rakers MIN-trans – min. transport width of 1.60/2.20 m

· 	 Steel pinions, hypoid transfer

· 	 The one-traction hook-on device

· 	 12 rakers on 1 working case, tangential conducting

· 	 Hydraulic adjustment of working width and rise of cases

· 	 The high raising of fingers at turn and transportation

· 	 Wheels are located close to raker’s fingers

· 	 Adjustment of an inclination sections

· 	 Roll-generator with roll stacking sideways S 1810 Pro

Advantages:

· 	 Optimum width of capture for a tractor from 40 kw/55 h.p.

· 	 The chassis with rotary wheels, the maximal stability of work, the minimal transport width

· 	 The closed reducer capsule-type with liquid greasing

· 	 Demountable rakers

· 	 Vario control has the minimal radius of turn

· 	 Unattended rakers, steel bearings

· 	 Rollers directing 47 mm

· 	 A cardan shaft with the increased corner of turn

· 	 Adjustment of height of work of each section

· 	Stepless updating of rakers’ work

· 	 Rise of working cases at turn up to 50 sm

· 	 Feed-harvesting combines JF-STOLL

A milk cow is required in 4 times of more energy, than dead-cow at efficiency 30 l/day. Therefore high quality of forages is required. The daily period of chewing a milk cow makes approximately 10 hours with a high yield of milk. Well crushed rough forages reduce time of chewing on 20 %. Therefore the need for nutrients is completely provided, that reduces need for the concentrated forages.

All machines are equipped with tungstic covering knifes, a tool-grinding stone with fast installation, a reverser opportunity, a anti-cutting plate with a tungstic covering with an opportunity of a turn on 180º. A rotor knifes are located on section for fast replacement. High efficiency is provided also with a wide rotor. Equipment by a grassy and corn harvester is possible. By all sorter machines hydraulic rise is established. The combine prepares forages as to straight lines combining, and selecting with the subsequent crushing shaky. Moving apart of feeding shaft provide high efficiency of a crushing drum. Cutting in a direction of emission reduces power consumption on 25 - 50 %.

Feed-harvesting combines KRONE

Self-propelled field grinder BiG X

BiG X is a self-propelled feed-harvesting combine with exact length of cutting. Speed of movement on road is 40 km/hours in serial execution. Owing to the innovative concept of a hydrostatic drive and movement characteristics as at the easy car, the combine moves on lower turns of the engine more quickly that allows to save up to 25 percent of fuel. The pressing roller hydraulic drives and an opportunity to adjust length are sharp from a cabin, not interrupting movement. The newest technologies, high working comfort, crushing quality of the highest level.

Sorter EasyFlow

Two sorter models of KRONE firm have capture width of 3 m or 3.8 m. With six rakers and distance between teeth of 55 mm, under any conditions, the sorter works loss-free and does not pass any stalk. The strong and firm design does EasyFlow serial sorter by the heavy-duty unit.

Copying of the ground’s relief: all feed-harvesting prefixes always faultlessly copy the ground’s relief by means of a pendular frame. For crossing on other field, lateral copying wheels are cleaned by means of hydraulic system.

EasyFlow-sorter works without the complex mechanism of rakers control, i.e. there is no set of the details in a design subject to intensive deterioration these are a racetrack and rollers rakers. Feature of the design is the wavy segment in immersing rakers zone and the increased rotation rakers working speed is allowed to refuse the mechanism of rakers control. There are no problems with winding fodder weight more. For this unit reliable and productive selection is characteristic. The sorter equipment also impresses: it is equipped by six rakers, and their consoles have an additional support. Other technical details: a sorter hydraulic drive with stepless change of rotation frequency, hydraulic copying wheels control for movement on roads, hydraulically lifted clamping roller, and also separate accident protection devices for a sorter and submitting screw.

Hydraulic drive with a greater range of the rotation frequency. The rotation frequency of from 300 and up to 700 rev/min is adjusted stepless from a cabin. Or it is possible to activate a automatic adjustment mode of the rotation frequency to speed of the machine movement, and to use greater opportunities BiG X in full valume.

Harvester of direct cut XDisc

The harvester of direct cut XDisc is equipped mowing disk by mechanism EasyCut. The fodder weight is mowed down with the highest quality of a cut and go on submitting screw in diameter of 0.90 m. Big screw reliably transports as well heavy long stalk weight to feeding rollers of a feed-harvesting combine. The rotation frequency of the cutting device can be adjusted stepless by means of a hydraulic drive directly from a cabin.

Width of capture is 6.20 m. Direct cleaning of silage weight or a biomass. Closed and checked up a mowing bar thousand times.