Table of contents

TECHNICAL SPECIFICATION	  9

GENERAL INFORMATION 	9

SPECIFICATIONS.	…………...10

CAPACITIES	 12

### RUNNING YOUR VEHICLE________________

THE KEYS 	 15

DOORS	 15

HOOD 		 17

LUGGAGE COMPARTMENT	17

FUEL GAUGE, FUEL FILLER CAP

AND FILLING THE CAR WITH FUEL 	 19

CENTRAL LOCKING	19

CENTRAL LOCKING

REMOTE CONTROL	20

IMMOBILIZER	20

FUEL SYSTEM

SAFETY SWITCH	21

STEERING COLUMN 	22

FRONT SEATS 	22

REAR SEAT, LUGGAGE COMPARTMENT

CAPACITY ENLARGEMENT 	23

SAFETY BELTS	24

SAFETY AIR BAGS 	25

GEARSHIFT LEVER

(MECHANICAL GEAR) 	26

GEARSHIFT SELECTOR (AUTOMATIC TRANSMISSION) 	26

PARKING BRAKE 	28

IGNITION SWITCH	.	28

CONTROLS AND INSTRUMENTATION 	13

CONTROLS	 13

INSTRUMENT CLUSTER 	 14

___________________________________________ 15

HAZARD FLASHER 	29

HORN SIGNAL 	29

ELECTRONIC WATCH	29

DOME LIGHT AND DASH PANEL

DIMMER	29

EXTERIOR LIGHTS AND TURN SIGNALS 	30

WINDSHIELD AND REAR WINDOW

WASHERS AND WIPERS 	33

WINDSHIELD AND REAR WINDOW DEFROSTER 	34

HEATING, VENTILLATION AND

AIR CONDITIONING	34

UTILITY COMPARTMENT		37

WINDOW RAISERS 	38

REAR VIEW MIRRORS 	39

CIGARETTE LIGHTENER AND ASH TRAYS 	39

SUNLIGHT SHIELDS 	'	40

ENGINE START	41

ANTI-LOCK

BRAKE SYSTEM (ABS)	41

TRACTION CONTROL SYSTEM (ТСS) 	41

ELECTRONIC ROAD HOLDING SYSTEM

Elektronisches Stabilitatsprogramm (ЕSР)	42

TOWING 	42

SERVICE, MAINTENANCE AND REPAIR SAFETY INSTRUCTIONS	43

SERVICING	45

BEFORE DRIVING 	47

WASHING FLUID REFILL 	47

WIPERS REMOVING  	48

ENGINE OIL LEVEL CHECK 	48

ENGINE OIL CHANGE AND OIL FILTER REPLACEMENT.…. ... 49

BRAKE SYSTEM CHECK	51

EXHAUST SYSTEM

CHECK 	52

TRANSMISSION, SUSPENSION

AND STEERING CHECK 	53

IGNITION PLUGS CHECK AND REPLACEMENT 	54

AUTOMATIC TRANSMISSION SERVICING

RECOMMENDATIONS……………………………………………….	.55

MECHANICAL TRANSMISSION GEAR OIL

LEVEL CHECK	.56

ENGINE COOLANT LEVEL CHECK 	.56

ENGINE COOLANT CHANGE 	.57

POWER STEERING

FLUID LEVEL CHECK 	.59

BRAKE FLUID

LEVEL CHECK…………………………………………………………. 	.59

BRAKE SYSTEM BLEEDING,
BRAKE FLUID CHANGE 	.60

CLITCH HYDRAULIC DRIVE PUMPING 	61

AIR FILTER

REPLACEMENT 	62

PASSENGER COMPARTMENT

VENTILATION FILTER REPLACEMENT	63

FUEL FILTER REPLACEMENT 	64

ENGINE AUXILLIARY BOOSTERS DRIVING BELT INSPECTION AND REPLACEMENT

FOR Zetec-E  1,8i/2,0i ENGINES	65

ENGINE AUXILLIARY BOOSTERS DRIVING BELT INSPECTION AND REPLACEMENT

FOR Duratec 1,6i ENGINES	67

ENGINE VALVE TIMING DRIVING BELT

INSPECTION FOR  Zetec-E  1,8i/2,0i ENGINES	68

ENGINE VALVE TIMING DRIVING BELT

REPLACEMENT FOR  Zetec-E  1,8i/2,0i ENGINES………………….	69

BATTERY SERVICING 	72

WHEELS AND TIRES INSPECTION 	74

WHEEL REPLACEMENT	75

FOUR WHEEL ROTATION 	76

KEY CELL REPLACEMENT	76

Zetec-E  1,8i/2,0i ENGINE VALVE EXPANSION

CLEARANCES INSPECTION AND ADJUSTMENT ………………….	77

CARING FOR YOUR VEHICLE__________________________________________________

80

WASHING YOUR VEHICLE 	80

KEEPING AND PROTECTION OF THE PAINTED SURFACES	81

CLEANING THE PASSENGER COMPARTMENT 	83

WHEELS AND TIRES 	83

GETTING PREPARED TO THE OFFICIAL CHECKUP	84

PREPARING TO CHECKUP 	84

LIST OF CONDITIONS AND FAILURES

WHEN DRIVING YOUR VEHICLE IS FORBIDDEN 	85

OFFICIAL CHECKUP

GENERAL INFORMATION……………………………………….. 86

VEHICLE REPAIR	87

DURATEC 1,6i ENGINE 	87

DESIGN DESCRIPTION 	87

OIL PRESSURE GAUGE REPLACEMENT 	89

ENGINE CYLINDER HEAD

COVER GASKET REPLACEMENT 	90

CRANKSHAFT FRONT PACKING GLAND REPLACEMENT 	91

CRANKSHAFT REAR PACKING GLAND REPLACEMENT	91

REMOVING THE OIL PAN AND

CLEANING THE OIL INTAKE GRID 	92

ENGINE SUPPORTS REPLACEMENT 	93

ENGINE REMOVING AND MOUNTING 	94

RECOMMENDATIONS FOR ENGINE REPAIR 	98

ZETEC-E ENGINE 	 108

DESIGN DESCRIPTION	 108

OIL PRESSURE GAUGE REPLACEMENT	 109

CAMSHAFT PACKING GLAND REPLACEMENT 	 109

CRANKSHAFT FRONT PACKING GLAND REPLACEMENT	 111

CRANKSHAFT REAR PACKING GLAND REPLACEMENT	 112

REMOVING THE OIL PAN AND

CLEANING THE OIL INTAKE GRID	 112

ENGINE SUPPORTS REPLACEMENT	 114

ENGINE REMOVING AND MOUNTING	 117

RECOMMENDATIONS FOR ENGINE REPAIR	 118

FUEL SYSTEM	 119

DESIGN DESCRIPTION 	 119

AIR FILTER REMOVING AND MOUNTING	 121

FUEL SYSTEM PRESSURE CHECK  	 121

FUEL TANK REMOVING AND MOUNTING 	 122

FUEL PUMP REPLACEMENT	 124

FUEL INDICATOR GAUGE REPLACEMENT 	 126

FUEL DISTRIBUTOR REMOVING AND MOUNTING 	 127

INJECTORS INSPECTION AND REPLACEMENT	 128

PRESSURE REGULATOR REPLACEMENT 	 128

THROTTLE CONTROL CABLE REPLACEMENT……….....…….. 129

THROTTLE VALVE HOUSING

REMOVING AND MOUNTING 	 130

Zetec-E  1,8i/2,0i ENGINE IDLE REGULATOR

REMOVING AND MOUNTING  	 130

Duratec  1,6i ENGINE IDLE REGULATOR

REMOVING AND MOUNTING	 131

RECEIVER REMOVING AND MOUNTING	 131

GASOLINE VAPOR RECOVERY SYSTEM	 133

ENGINE CONTROL SYSTEM 	 134

DESIGN DESCRIPTION	 134

ENGINE CONTROLLER

REMOVING 	 138

ENGINE CONTROL SYSTEM

RELAYS AND FUSES 	 139

TIMING GAUGE REPLACEMENT 	 139

TEMPERATURE GAUGE REPLACEMENT 	 140

THROTTLE POSITION GAUGE

INSPECTION AND REPLACEMENT	 141

Zetec-E  1,8i/2,0i CAMSHAFT POSITION GAUGE
REPLACEMENT 	 142

Duratec 1,6i CAMSHAFT POSITION GAUGE
REPLACEMENT	143

OXYGEN CONCENTRATION GAUGE REPLACEMENT,	.143

Duratec 1,6i AIR TOTAL PRESSURE AND TEMPERATURE

GAUGE REPLACEMENT	144

Zetec-E  1,8i/2,0i AIR MASS FLOW GAUGE

REPLACEMENT 	144

VELOCITY GAUGE REPLACEMENT	144

IGNITION CONTROLLER REPLACEMENT 	145

ENGINE COOLING SYSTEM 	146

DESIGN DESCRIPTION	146

COOLANT TEMPERATURE GAUGE

REPLACEMENT 	147

TEMPERATURE REGULATOR REMOVING, INSPECTION

AND MOUNTING	148

COOLANT RESERVOIR REMOVING AND MOUNTING 	148

RADIATOR COOLING FAN MOTOR REPACEMENT. ………………. 149

RADIATOR REMOVING AND MOUNTING 	150

COOLANT PUMP

REMOVING AND MOUNTING	151

EXHAUST SYSTEM	152

DESIGN DESCRIPTION	152

EXHAUST SYSTEM SUSPENSION CUSHION PADS

REPLACEMENT 	153

RECEIVER PIPE REPLACEMENT	153

EXHAUST SYSTEM ELEMENTS

REPLACEMENT	154

EXHAUST MANIFOLD REMOVING AND MOUNTING	155

CLUTCH 		156

DESIGN DESCRIPTION	156

CLUTCH PEDAL STROKE CHECK	156

CLUTCH DRIVEN DISK AND HOUSING REPLACEMENT 	157

CLUTCH PEDAL GAUGE REPLACEMENT 	158

CLUTCH HYDRAULIC DRIVE HOSE REPLACEMENT	158

REPLACEMENT OF THE CLUTCH HYDRAULIC DRIVE

WORKING CYLINDER AND RELEASE BEARING ………………..158

CLUTCH PEDAL AND CLUTCH HYDRAULIC DRIVE MAIN

CYLINDER REMOVING AND MOUNTING 	159

GEAR BOX 	160

DESIGN DESCRIPTION	160

GEAR BOX CONTROL GEAR

ADJUSTMENT	161

FRONT WHEEL DRIVING SHAFT GLAND REPLACEMENT 	162

GEAR BOX REMOVING AND MOUNTING	162

GEAR BOX REPAIR RECOMMENDATIONS 	164

GEAR BOX CONTROL GEAR

REMOVING AND MOUNTING 	164

GEAR BOX CONTROL GEAR CABLES

REPLACEMENT 	164

AUTOMATIC TRANSMISSION 
INSPECTION 	165

FRONT WHEEL DRIVING SHAFTS 	166

DESIGN DESCRIPTION 	 166

FRONT WHEEL DRIVING SHAFTS

REMOVING AND MOUNTING 	 166

OUTER BALL-AND-SOCKET (EVEN ANGULAR VELOCITIES)

JOINT REMOVING	167

INNER BALL-AND-SOCKET (EVEN ANGULAR VELOCITIES)

JOINT REMOVING	169

INTERMEDIATE BEARER BEARING

REPLACEMENT 	170

FRONT WHEEL SUSPENSION	171

DESIGN DESCRIPTION	171

FRONT WHEEL ANGLES OF INCIDENCE	172

FRONT SUSPENSION ARM

REMOVING AND MOUNTING 	173

SHOCK ABSORBER ASSEMBLY

REMOVING AND MOUNTING	174

SHOCK ABSORBER ASSEMBLY REPAIR ..:	175

TRANSVERSE STABILIZER REST

REPLACEMENT	177

TRANSVERSE STABILIZER ROD

REPLACEMENT	177

FRONT HUB BEARING REPLACEMENT	178

REAR WHEEL SUSPENSION	180

DESIGN DESCRIPTION	180

SHOCK ABSORBER REPLACEMENT	181

SUSPENSION SPRING REPLACEMENT	182

UPPER SUSPENSION ARM REPLACEMENT	183

LOWER FRONT SUSPENSION ARM REPLACEMENT	184

TRAILING ARM REPLACEMENT	184

LOWER BACK SUSPENSION ARM REPLACEMENT	185

TRANSVERSE STABILIZER REST

REPLACEMENT	185

TRANSVERSE STABILIZER ROD

REPLACEMENT	186

SUSPENSION ARM POSITIONS ADJUSTMENT	186

REAR WHEEL SUSPENSION REMOVING AND MOUNTING 	187

HUB BEARING REPLACEMENT	188

REAR WHEEL ANGLES OF INCIDENCE	188

STEERING 	189

DESIGN DESCRIPTION	189

DEAERATION OF POWER STEERING HYDRAULIC

BOOSTER	190

STEERING WHEEL REMOVING AND MOUNTING 	190

STEERING ROD END REPLACEMENT	191

STEERING ROD REPLACEMENT 	192

POWER STEERING HYDRAULIC BOOSTER

PRESSURE GAUGE REPLACEMENT 	192

POWER STEERING HYDRAULIC BOOSTER

PUMP REMOVING 		193

STEERING GEAR REMOVING AND MOUNTING 	194

STEERING TUBE REMOVING AND MOUNTING	196

BRAKE SYSTEM	198

DESIGN DESCRIPTION	198

FRONT WHEEL BRAKE PADS

REPLACEMENT	199

REAR WHEEL BRAKE PADS

REPLACEMENT (DRUM-TYPE BRAKE)	201

BRAKE SYSTEM MAIN CYLINDER

REMOVING AND MOUNTING	203

VACUUM SERVO REMOVING AND MOUNTING 	204

DISK-TYPE BRAKE CALIPER REPLACEMENT	205

BRAKE DISK REPLACEMENT	205

FRONT WHEEL BRAKE HOSE REPLACEMENT	205

REAR WHEEL DRUM-TYPE BRAKE

CYLINDER REPLACEMENT	206

REAR WHEEL BRAKE HOSE REPLACEMENT	207

PARKING BRAKE CONTROL CABLE

HEAD REPLACEMENT	207

PARKING BRAKE ADJUSTMENT	208

WHEEL ROTATION SPEED GAUGES REPLACEMENT	209

ELECTRICAL EQUIPMENT 	210

General information	210

electrical network check	210

ignition switch	211

junction blocks, fuses and relays	211

alternator	.	214

design description	214

Zetec-E 1,8i/2,0i engine alternator removing	215

Zetec-E 1,8i/2,0i engine alternator

voltage regulator replacement	.	217

Duratec 1,6i engine alternator removing	218

Duratec 1,6i engine alternator

voltage regulator replacement	219

STARTER	220

Design description	220

Zetec-E 1,8i/2,0i engine starter removing	220

Duratec 1,6i engine starter removing	221

Starter assembling and disassembling	222

BULBS, SOUND AND LIGHT SIGNALS ...................................… 225

Headlamp bulbs replacement 	225

Headlamp removing	226

Headlamps power aiming electric drive replacement	227

Fog lamp removing, bulb replacement 	227

Turn signal lamp removing, bulb replacement 	228

Backup switch replacement	228

Tail lights removing and mounting, bulbs replacement	229

Luggage compartment lamp

removing and mounting, bulb replacement,

for sedan car body  	231

High-mount brake lamp

removing, bulbs replacement	232

License plate lamps removing,

Bulbs replacement 	233

Dome lamp removing,

Bulb replacement	234

Utility compartment lamp removing,

bulb replacement	234

Steering-tube-mount controls removing and mounting	234

Hazard flasher switch removing 	235

Horn removing and mounting	235

WATCH REMOVING AND MOUNTING 	236

WINDSHIELD AND REAR WINDOW

WASHERS AND WIPERS	 236

Windshield wiper removing and mounting 	237

Washer electric pump removing	239

Rear window wiper removing and mounting	240

INSTRUMENTATION 	241

Instrument cluster removing	241

Instrument cluster Dimmer bulbs replacement 	242

SAFETY AIR BAGS CONTROLLER

REMOVING AND MOUNTING 	242

AUDIO SYSTEM REMOVING AND MOUNTING 	243

Loudspeaker removing	243

BODY 	244

DESIGN DESCRIPTION	244

RADIATOR CASE REMOVING 	244

REMOVING OF THE HOOD LOCK AND IT’S ACTUATOR	245

HOOD REMOVING	246

FRONT FENDER SHIELD REMOVING 	246

FRONT BUMPER REMOVING 	247

FRONT FENDER REMOVING 	'.	248

REAR-VIEW SIDE MIRROR REMOVING	249

FRONT DOOR LINING (UPHOLSTERY) REMOVING 	249

FRONT DOOR WINDOW REMOVING 	250

FRONT DOOR WINDOW RAISER GEAR

REMOVING 	251

FRONT DOOR LOCK REMOVING 	252

FRONT DOOR

REMOVING, MOUNTING AND ADJUSTMENT 	254

REAR DOOR LINING (UPHOLSTERY) REMOVING	255

REAR DOOR WINDOW REMOVING	:	256

REAR DOOR WINDOW RAISER GEAR

REMOVING	257

REAR DOOR LOCK REMOVING	258

REAR DOOR

REMOVING, MOUNTING AND ADJUSTMENT	259

REAR BUMPER REMOVING	260

TRUNK LID LOCK AND REAR DOOR LOCK

REMOVING	261

REAR DOOR

REMOVING, MOUNTING AND ADJUSTMENT 	262

TRUNK LID

REMOVING, MOUNTING AND ADJUSTMENT	264

FRONT SEAT REMOVING	265

REAR SEAT REMOVING 	266

SAFETY BELTS REMOVING 	.	267

FLOOR HEADING JACKET REMOVING 	268

DASH PANEL REMOVING 	269

VENTILATION, HEATING AND

AIR-CONDITIONING SYSTEM	275

DESIGN DESCRIPTION 	275

HEATER FAN REPLACEMENT	276

HEATER ADDITIONAL RESISTOR REPLACEMENT …………. ...276

HEATER RADIATOR REPLACEMENT 	277

HEATER CONTROL PANEL

REMOVING AND MOUNTING	278

TROUBLESHOOTING________________________________________280

ENGINE AND IT’S SYSTEMS 	280

CLUTCH	289

MECHANICAL GEAR-BOX	290

AUTOMATIC TRANSMISSION 	291

FRONT WHEEL DRIVING SHAFTS	292

BRAKE SYSTEM 	293

SUSPENSION AND STEERING	294

ELECTRICAL EQUIPMENT 	296

APPENDIXES

REPAIR TOOLS 	300

IMPORTANT THREADED CONNECTIONS

TORQUES OF TIGHTENING	302

FUEL, LUBRICANTS AND

WORKING FLUIDS 	304

BULBS 	305

ELECTRICAL EQUIPMENT LAYOUTS 	306

Alternator wiring diagram	306

Engine starter system

for mechanical transmission	306

Engine starter system

for automatic transmission 	307

Fuel pump wiring diagram	307

Injectors and Idle controller wiring diagram …………………..... 308

Air mass flow gauge and oxygen concentration gauge

wiring diagram 	308

Coolant temperature gauge and throttle position gauge

wiring diagram	309

Immobilizer wiring diagram 	309

Cooling system radiator fan wiring diagram

for the car not equipped with A/C system	309

Cooling system radiator fans wiring diagram

for the car equipped with A/C system	310

Wiring diagram for adsorber blasting solenoid valve, camshaft positions gauges, crankshaft rotary speed gauge, power steering hydraulic booster

pressure gauge 	310

Wiring diagram for speed gauges and

clutch pedal	311

Ignition system layout	311

Automatic transmission electrical equipment

layout 	312

ABS + TCS controller

wiring diagram	313

ABS controller

wiring diagram	313

ABS + TCS + ESP controller

wiring diagram 	314

Wheel rotation speed gauges

and ABS indicator lamp wiring diagram	314

Wheel rotation speed gauges,

ABS and TCS indicator lamps wiring diagram	315

Headlamps power aiming electric adjuster wiring diagram 	316

Headlamps wiring diagram	317

Fender lights wiring diagrams,

for wagon car body 	317

____________________________ 300

Fender lights wiring diagrams,

for sedan car body	318

Fender lights wiring diagrams,

for hatchback car body 	318

Brakelamps wiring diagram,

for automatic transmission car 	319

Brakelamps wiring diagram,

for the car equipped with automatic transmission and ESP 	319

Brakelamps wiring diagram,

for the car equipped with mechanical gear-box and ABS 	320

Brakelamps wiring diagram,

for the car equipped with mechanical gear-box and ESP	320

Hazard flasher and turn signals

wiring diagram 	321

Tail fog lamps wiring diagram …………………………………...... 322

Head and Tail fog lamps

wiring diagram 	323

License plate lamps

Wiring diagram	324

Backup lamps wiring diagram,

for the car equipped with mechanical gear-box	324

Backup lamps wiring diagram,

for the car equipped with automatic transmission 	324

Dome lights wiring diagram	325

Luggage compartment lamps wiring diagram,

for sedan and hatchback car bodies…………………………..... 325

Luggage compartment lamps wiring diagram,

for wagon car body	326

Horns wiring diagram 	326

Door terminal switches wiring diagram

(with central lock)	327

Power window

electric actuators wiring diagram (for front doors only)	327

Left front door power window

electric actuator wiring diagram	328

Right front door power window

electric actuator wiring diagram	329

Central lock wiring diagram 	329

Rear door power window

electric actuators wiring diagram 	330

Windshield wiper wiring diagram

(for sedan car body)	331

Windshield and rear window wipers wiring

diagram (for wagon and hatchback car bodies)	332

Headlamp washers and windshield washer injector heating 
elements wiring diagram	333

Power rear-view side mirrors

electric actuator and electric heater wiring diagram 	333

Front seats heating elements

wiring diagram	334

A/C system compressor coupling

wiring diagram	334

Driver seat vertical adjustment electric actuator

wiring diagram 	334

Front door power locking actuators

wiring diagram (central locking with double locking) 	335

Alarm system wiring diagram	336

Immobilizer gauge wiring diagram 	336

Safety air bags controller

wiring diagram 	337

Heater fan wiring diagram 	338

Rear door power locking actuators

and door terminal switches wiring diagram

(central locking with double locking) 	338

Heating, ventilation and

A/C system control panel wiring diagram	339

Instrument cluster electrical layout (fuel shortage, battery

charge, check engine, step-up gearing indicator lamps)	340

Instrument cluster electrical layout (turn signals and high

beams indicator lamps, dash panel dimmer lamps) 	341

Instrument cluster electrical layout (brake

system and engine oil pressure alarm lamps) 	342

Delay controller, heating system,

ventilation system and A/C system electrical layout	343

Delay controller and

instrument cluster electrical layout	343

Delay controller,

interior lights and window wipers electrical layout 	343

# BRAKE SYSTEM

The front brake gear: 1 — outer brake pad; 2 — brake disk (ventilated); 3 —brake pads guide; 4—inner brake pad; 5 — brake caliper with the working cylinder; 6 — guide pin (covered by the protector with cap); 7 — brake hose nozzle; 8 — cylinder bleeding nipple; 9 — bleeding nipple protection cap; 10 — front suspension steering knuckle

Rear drum-type brake gear: 1 — pivot (wheel hub axle); 2 — brake drum; 3 — wheel mounting studs; 4 — lower tie spring; 5 — rear brake pad; 6 — parking brake operating lever; 7 — brake pad clamping clip; 8 — clamping clip rod; 9 — parking brake operating lever release spring; 10 — upper tie spring; 11 – working cylinder; 12 — front brake pad; 13 – distance bar; 14 — brake shield; 15 — parking brake control cable end.

DESIGN DESCRIPTION

The brake system is hydraulic, double-circuit (with diagonal circuits distribution) system. The ventilated disk-type brake gears are installed for front wheels; the disk-type or the drum-type brake gears can be installed for rear wheels depending on the modification.

The front brake gear is a piston-type gear with the floating brake caliper. The rear disk-type brake gear is similar to the front one, but it is smaller. The rear drum-type brake gear has a double-piston cylinder and two brake pads. The clearance between the pads and the drum is automatically adjusted by means of the distance bar with brake pads regulator installed on it. The front…

Remove the hose with elastic holder from the bracket.

Tie the caliper up to the spring by wire or rope.

Similarly unscrew and remove the upper guide pin.

...and remove it.

Take the caliper aside, watching the brake hose not to be overstretched or over-twisted...

Remove the outer brake pad with spring clip from the caliper.

Move the inner brake pad taking it’s spring clip out from the piston cavity...

... and remove the inner brake pad.

Take the spring clip end out from the brake pad bracket by pliers...

... and remove the clip from the brake pad.

Mount the clip on the new brake pad.

Clean the brake gear parts from dust and rust, especially the brake pad seats in the caliper and the brake pads guide on the steering knuckle.

It is forbidden to use gasoline or diesel fuel for cleaning the brake gears.

Press the brake pad to the piston.

Mount the inner brake pad bringing the petals of spring clip into the piston cavity.

Mount the outer brake bar into the caliper pressing it to the clamp.

Mount the caliper to its place and tighten the guide pins with the

28 Nm torque.

Mount the protector caps to their places and remove the wire that holds the caliper. Insert the brake hose holder into the bracket.

Hocking the spring clip by a screwdriver, bring it behind the clamp lugs.

Unscrew the nuts that hold the brake disk, and mount the removed wheel on its place.

After the replacement of the brake pads on both front wheels you should press the brake pedal several times for setting the proper clearances between the brake pads and the disks.

Check the brake fluid level in the reservoir. Refill when necessary.

REAR WHEEL BRAKE PADS REPLACEMENT (DRUM-TYPE BRAKE GEAR)

Replacing the brake pads of one brake gear only would bring to irregular braking of the car rear wheels.

You should replace the brake pads of the right and left rear wheel brake gears at the same time.

If brake fluid in the reservoir is on the Maximum level, take some fluid out from the reservoir by rubber pear in order to

avoid brake fluid run out from the reservoir when you push the pistons into the cylinder. Parking brake lever should be downed to stop (the car is unbraked). Remove the rear wheel (see «Wheel replacement», p. 75).

Lifted part of the car should be rested on the reliable factory made straddle.

Remove the wheel rotation speed gauge from the car equipped with ABS (see «Wheel rotation speed gauges replacement», p. 209).

Unscrew four bolts holding the wheel hub pivot to the longitudinal lever on the back side of the brake shield by 13 mm head hex-nut wrench.

Remove the brake drum together with the pivot.

It could be difficult to remove the drum if there is a high rib on the drum working surface because of the wear. In this case you should ease the tension of the parking brake cable (see «Parking brake adjustment», p. 208).

Body

DESIGN DESCRIPTION

Body is all-metal, welded, integral, it is made in three versions: 4-doors sedan, 5-doors hatchback and wagon. Non-removable parts of the body are made from steel sheets of different thickness and jointed by welding.  The body bearing elements (such as side members, sills, pillars and cross members) have box-like section.  Baffles and reinforcements are installed inside some of the elements. Front fenders are removable; they are screwed to the body by cut-screws. Front panel is also removable; it is fixed to the splash aprons and side members by bolts.

Hack the eyelets by a screwdriver....

The doors, hood, trunk lid (sedan), rear door (hatchback and wagon) are installed on hinges. Their positions in the openings are adjusted. Special safety enforcements are embedded in the front and rear doors for the protection of passengers from side blow. The windshield is a glass sandwich; it is polished and pasted in the body opening, as the rear window as well (for sedan body cars). Hatchback and wagon rear window is pasted in the rear door opening. Side glasses are also pasted in the body openings.

The door windows are drop-type; they are equipped with manual gears or electric actuators.

The front seats are separated; you can adjust them by moving forward and back and by changing of the seatback tilt angle.

You can raise or lower the driver seat cushion and adjust its lumbar support.

All the seats are equipped with the safety belts.

REMOVING OF THE RADIATOR CASE

Open the hood...

...unscrew three screws of the panel fixing eyelets by a Phillips screwdriver.

...and pull them out of the holes.

Remove the panel, taking its four clips out of the engagement with the radiator case.

Unscrew the radiator case central clip lock bar screw by a Phillips screwdriver.

Unscrew two radiator case lower fixing bolts by 10 mm head hex-nut wrench.

Washers are installed under the bolt heads.

4. Remove the hose with elastic holder from the bracket.

5. Unscrew the bleeding nipple on ½-¾-turn. Old (dusty) brake fluid starts to bleed from the hose. The brake pedal has to reach smoothly to stop. As soon as brake fluid stops to bleed, tighten the bleeding nipple.

- Watch permanently for brake fluid level in the reservoir. Do not allow the level drop below MIN ; add fresh brake fluid when necessary.  Repeat the steps 4 and 5 until fresh (clear) brake fluid bleeds from the hose.

- Change brake fluid in the left front wheel brake gear the same way, and then in the second circuit (firstly in the left rear wheel brake gear, and then in the right front wheel brake gear).

- Press the brake pedal several times. The pedal stroke and resistance should be the same on every pedaling.  Some air has got in the brake system if those conditions are not satisfied. If so, it is necessary to bleed the brake system (see «Brake system bleeding»).

- It is obligatory to put the protection caps on the bleeding nipples after brake fluid change.

10.	Add brake fluid to the reservoir until the level reaches MAX and tighten the reservoir cap.

FRONT WHEEL BRAKE GEARS

Brake pads

replacement

Minimum allowed brake pad wear facing thickness is 1,5 mm. Replace brake pads when the following occurs: brake pad wear facing thickness is less than allowed; facing surface is greasy; facing is not tightly fixed to the base; facing has deep grooves and chips.

WARNINGS

Do not use petrol, diesel or other mineral solvents for cleaning of the brakes.

Replace brake pads of both front wheel brakes at the same time.

It is forbidden to interchange the inner and outer brake pads, and to interchange the brake pads of the right and left wheel brakes. It could bring to irregular braking.

- Disconnect the cable from «-» battery terminal.

- Brake the car by parking brake and put the stops under the rear wheels. Remove the front wheel and clean the brake gear from dust.

- If brake fluid in the reservoir is on the MAX level, take some fluid out from the reservoir by rubber pear.
Otherwise it would overflow when the new brake pads would be installed.

6. Unscrew the upper guide pin fixing bolt, holding it by hex-nut wrench.

7. Turn the clamp housing down around the lower pin axe.

8. Mark the brake pads, if you presume to reinstall them back.

9. Remove the brake pads.

WARNING

10. Check the thickness and condition of the brake pad wear facings.

Wear facing surfaces are not to be greasy, having deep grooves or chips. The facing should be tightly fixed to the pad base.

HELPFUL HINT

If under the next regular check the thickness of the facings is close to the minimum allowed, you can use them, but their service life is close to the end. It is up to you to choose: either you replace the pads right away, or watch for their thickness permanently.

6. Turn the engine oil filler cap 90° counter clock-wise and remove it.

HELPFUL HINT

7. Pour the new engine oil checking the level by indicator (dipstick).

TDC marks location

2. Unscrew the oil filter by special wrench.

3. If you do not have the wrench and cannot to unscrew the filter by hands, punch a hole in the filter by screwdriver and unscrew the filter using the screwdriver as a lever. You should punch the hole closer to the bottom in order to not to damage the threaded connector of the engine.

4. Lubricate the sealing ring of the new oil filter by engine oil and fill the new filter with engine oil until half-filled before installation.

5. Screw the new filter on by hands without any tools.

TDC marks are applied on the camshaft gear pulley (lug) and on the camshaft driving belt back cover (tab).

8. The oil level should be near MAX mark. Start the engine and let it idle for some minutes. Turn the engine off, check the oil level, refill when necessary.

SETTING THE FIRST

CYLINDER PISTON IN

COMPRESSION STROKE

TOP DEAD CENTER (TDC)

POSITION

Moreover, the marks are applied on the flywheel (notch line) and on the clutch housing back shield bar (triangular cutout). Gear box is removed for obviousness.

WARNING

Turn the crankshaft taking by the pulley fixing bolt only (it is forbidden to turn the crankshaft taking by the camshaft pulley)

Section 1. Vehicle design

Section 2. Running recommendations

Section 3. Roadside emergencies

Section 4. Engine

Section 5. Transmission

Section 6. Chassis

Section 7. Steering

Section 8. Brake system

Section 9. Electrical equipment

Section 10. Body

Section 11. VAZ-21083-20 and VAZ-21093-20 vehicles

(equipped with the fuel injection system) features

Section 12. Carburetor engine cars toxicity abatement system

Section 13. Caring for your vehicle

Section 14. Purchasing of spare parts

Section 15. Trip to service station

Section 16. Driving in winter conditions

Section 17. Preparing to checkup

Appendixes

Electrical equipment layouts

# Text boxes

TABLE OF CONTENTS

## CAR    REPAIR

BRAKE    SYSTEM

TABLE OF CONTENTS

TABLE OF CONTENTS

TABLE OF CONTENTS

Unscrew the lower guide pin by 7 mm hex-nut wrench...

Remove the protector caps from both guide pins.

## CAR    REPAIR

BRAKE    SYSTEM

Additional marks are applied on the crankshaft gear pulley (dot) and on the engine oil pump cover (triangular cutout). Those marks can be seen only when the alternator driving pulley is removed.

TABLE OF CONTENTS

TABLE OF CONTENTS

TABLE OF CONTENTS

TABLE OF CONTENTS

BRAKE    SYSTEM

## CAR    REPAIR

## CAR    REPAIR

Remove the lock bar.

## CAR    REPAIR

BODY

This setting is made for not to break the setting of the engine timing phases when you do the works concerned with the removing of the camshaft driving belt. If you break the setting of the timing phases, the engine will not run properly. Set the TDC according to the mark on the camshaft pulley (when you set according to the marks on the crankshaft pulley or flywheel , the piston of either 1st, or 4th cylinder could be in TDC position). After that make certainly sure that the marks on the flywheel or crankshaft gear pulley (if the crankshaft alternator driving pulley is removed) coincide. If the mark on the flywheel or crankshaft gear pulley does not coincide, that means that the setting of the timing phases is broken (1st cylinder piston is not set in the TDC position). In this case remove the camshaft driving belt and turn the crankshaft until the marks coincide.

As it is uncomfortable to turn the crankshaft by the pulley fixing bolt, you can make it by the following ways: 1. Turn on a gear (the 4th is better) and give the car a drive slowly until the mark on the camshaft pulley coincides with the mark on the camshaft driving belt back cover. 2. Turn on a gear and lift one of the front wheels. Turn the lifted wheel until the mark on the camshaft pulley coincides with the mark on the camshaft driving belt back cover.

TABLE OF CONTENTS

5. Straighten out the tab of the tab washer of the upper guide pin fixing bolt.