Personal Safety Code

a) When using electric tools, be careful, mind your actions and follow common sense. Do not use electric tools when you are tired or under drugs, alcohol or medicament effect.

Careless use of electric tools can lead to painful injuries.

b) Use personal safety means. Always wear protective glasses.

Depending on the kind and use of electric tool, personal safety means such as respirators, a non-sliding protective footwear, a helmet or ear protective means reduce the risk of injuries.

c) Beware of tools unintended triggering. Before connecting an electric tool to the mains and/or an accumulator battery, taking it in hand or carrying it over, make sure it’s switched off.

In case your finger rests on the switch key when you carry the tool, or the tool turns to be switched on when you connect it to the mains, this can lead to injury.